## Slide 1
A brief
Introduction
To
GIS

## Slide 2
What is GIS?
Geographic Information System
“..integrated computer hardware and software that store, manage, analyze, edit, output, and visualize geographic data. Much of this often happens within a spatial database…In a broader sense, one may consider such a system also to include human users and support staff, procedures and workflows, the body of knowledge of relevant concepts and methods, and institutional organizations.”-Wikipedia
“Any system for capturing, storing, checking, and displaying data related to positions on the Earth's surface.” -National Geographic Education Encyclopedia
In a GIS, you connect data with geography
-GISgeography.com

## Slide 3
Expensive, commercial
Windows (but there are work-arounds)
More stable, consistent, compatible; less flexible, less customizable
Cannot open some QGIS files
Until this year, it was the ONLY way to run LAHARZ!
Free, open source
Windows, Mac, Linux, Android
More flexible, customizable (plug-ins, scripting), but can have bugs
Can open ArcGIS formatted files
Thanks to Keith Blair, there is now an open-source, stand-alone python version of LAHARZ!
Two popular GIS programs

## Slide 4: Two popular GIS programs
For this year’s course, we will use QGIS for the first time and the open-source version of LAHARZ on the VICTOR platform
However, the ArcGIS course materials (ArcMap and ArcPro) and LAHARZ code are still available and will be provided to you in the class files

## Slide 5
Vector Data
Raster Data
Points
Lines
Polygons
Representing Geographic Features
“Raster is faster;
Vector is correct-er”
Digital elevation models (DEMs), hillshades, satellite images are all rasters
Features like road networks, lakes, park boundaries, station locations, etc. are usually vectors (in ArcGIS these are shapefiles)

## Slide 6
Spatial Coordinates
(204654, 3984988)
Where is it?
FID | Shape * | Volcano | Instrument | Solar?
024 | point | Kilauea | Seismometer | Yes
Attributes
What is it?
GIS works when you combine geographic location with attribute information
and you display it with
scale, direction, and system of measurement

## Slide 7
Projections can preserve size, shape, and distance, but not all three at the same time!
Notes: Not a flat earth. Project reality onto a plane. There are many ways to do this. And none is close to perfect.
Polar coordinates to linear coordinates is complex math. Flattening can be achieved by sacrificing one or more:
Angular direction, area, distance, shape

## Slide 8
Geoid
  approximates mean sea level without winds or tides
Spheroid (ellipsoid)
  Mathematically idealized approximation of the size and shape of Earth
WGS84 datum
  World Geodetic System
  Defines an earth-centered coordinate system with the origin coordinate at the Earth’s center of mass
  Used by GPS and satellite data
https://en.wikipedia.org/wiki/World_Geodetic_System
Notes: And those projections assume a spheroid or an ellipsoid. When we know there are places on earth that are above and below sea level – the Tibetan Plateau, Mauna Kea. And sea level is also in flux. When you shrink down from global projections to a local projection that is tied to a local datum so that your local areas, distances, vectors are more accurate, there are even more mathematical ways to compute coordinate systems with datums. For the rest of this class, we are only going to work with Transverse Mercator and WGS84 datum. It’s not necessarily the best, but it works well as a standard when you’re looking at all the volcanoes around the world.

## Slide 9
Universal Transverse Mercator (UTM)
Divides earth into 60 zones and projects each to the plane as a basis for its coordinates
Specifying a location means specifying the zone and the x, y coordinate in that plane.
Uses a grid-based, cartesian system so calculating distances is easy (which is why we use it for ArcGIS versions of LAHARZ)
https://hub.arcgis.com/datasets/esri::world-utm-grid/explore?location
Google Earth: tools/options
For the ArcMap and ArcPro versions of LAHARZ, the DEM needs to be in UTM
For the VICTOR and stand-alone python versions, projections are handled internally

## Slide 10
SRTM
Space Shuttle Radar Topography Mission Survey
Collected for 11 days in February 2000
Radar “sees” through clouds
60° N to 56° S, free
X-band ~6cm wavelength
30-meter global dataset
Version 3 “MEASURES” released 2020
ASTER
Advanced Spaceborne Thermal Emission
and Reflection Radiometer (optical instrument) on Terra
4 million images 2000-2019
Data gaps: persistent clouds; filled with SRTM
83° N to 83° S, free
Optical stereo derived; elevations may include vegetation
30-meter global dataset
Version 3 released 2019
TerraSAR-X & Tandem-X
Pair of satellites flying in close formation
Collected over 6 years of 2010-2015
Radar “sees” through clouds
0° N to 0° S, free
X-band ~6cm wavelength
90-meter global dataset
(future release of 30 or 12 meters?)

## Slide 11: DEMs on VICTOR

## Slide 13
 | Precise | Not Precise
Not Accurate |  | 
Accurate |  | 
How much did my phone cost?
$400
$399.99
$3,999,999.999
$4,000,000
Precision Accuracy
=

## Slide 14
Which DEM would you want to use?

## Slide 15
2005
June 19, 2024
2023
Which DEM would you want to use?